## Slide 1: Development of Lyman Alpha Imaging Camera (LAICA) geocorona imaging device for PROCYON, ultrasmall deep space probe
Shingo Kameda et al from Rikkyou U, Tokyo U, and ISAS/JAXA
[JAXA]
http://laika.paina.jp/
http://kuma1117.cocolog-nifty.com/blog/images/2011/01/13/00001297.jpg

## Slide 2
PROCYON
mass：approx. 59kg
dimension：H630×W550×D550mm
to be launched in December 2014
[JAXA]
・additional payload on Hayabusa 2 to be part of PROCYON, ultrasmall deepspace probe
(Hydrogen) Lyman Alpha Imaging Camera
・1-2 weeks observation after launch (spatial resolution <0.4Re)
⇒imaging wide area distribution of geocorona (
field of view 25-300Re)
⇒further 3 months observation expected (
spatial resolution <2.4Re）
PROCYON軌道
PRoximate Object Close flYby with Optical Navigation

## Slide 3
What is geocorona
Exosphere：Outermost layer of Earth atmosphere (altitude >400km)
・main components：hydrogen and helium atoms
selective scattering of specific solar radiation of ultraviolet light
⇒ultraviolet glow engulfing whole Earth
hydrogen Ryman alpha line (121.6nm) is the brightest
太陽
：geocorona
geocorona distribution seen by Apollo 16 [Carruthers et al., 1976]

## Slide 4
Hydrogen atom density contour：equatorial (right) ,meridian (left) [Bailey and Gruntman, 2011]
Non-symmetry in day/night, N/S, morning/evening
TWINS borne LAD(Lyman Alpha Detector) observation
higher density in day side than night side in lower altitude
angular changes of hydrogen atom density
[Bailey and Gruntman, 2011]
similar densities in very high altitude bet. day side and night side
higher density in evening side than morning side
higher density in southern hemisphere
m
e
d
n
d
n
S
N
Geocorona spatial distribution

## Slide 5
Atomic orbits in exosphere
Exobase：lowest altitude where atoms do not collide
(400〜800km)
3 main atomic orbits in exosphere
  ① ballistic orbit : atoms shoot out of exobase at less than escape velocity and come back in
  ② escape orbit : atoms shoot out of exosphere and are lost
  ③ satellite orbit : scattered within closed orbit
in lower altitude ballistic atom are dominant
⇒at higher altitude satellite orbit becomes dominant
at very high altitude escape atoms
become dominant
③
①
②
exobase

## Slide 6
Magnetic storm and number of hydrogen atoms
Dst index(above)とTWINS/LAD 3〜8RE number of hydrogen atoms(below) [Bailey and Gruntman, 2013]
when storms
occur
⇒6-17% increase in number of hydrogen atoms
inside 3-8RE
temporal resolution: approx. 12 hours (one revolution is 12 hours)
unable to time-resolve changes in number of hydrogen atoms
in response to temporal changes of magnetic storm
LAD observation geometry
[Bailey and Gruntman, 2011]

## Slide 7
Observations until now mainly via earthbound satellites
⇒ geocorona extends up to 20RE
examples at far distance from earth include
⇒ only Mariner 5 [Wallace et al.,1970], Apollo 16 [Carruthers et al., 1976], Nozomi [Tsuchiya, 2003]
<objectives>
imaging of geocorona up to〜20RE
⇒hydrogen density at extreme altitudes
higher temporal resolution than earth bound satellites (1 hour)
⇒new insight into the loss process of earth atmosphere
Imaging of geocorona
as seen by Apollo 16 [Carruthers et al., 1976]
⇒difficult to obtain density distribution at extremely high altitude

## Slide 8: geocorona imaging-objectives
(1) Extremely high altitude(>8RE) geocorona(H Ly-α)distribution to be imaged
  latitude distribution of hydrogen atoms at high altitude in single image(Mariner 5: ~16RE, Apollo 16: ~10RE, Nozomi: ~24RE )
  Timing of observation: 7-14 days after launch
  ①quantising hydrogen atoms loss process by charge exchange reaction and photoionisation
Apollo 16 imaging of geocorona distribution [Carruthers et al., 1976]
(2) Temporal changes in high altitude geocorona and magnetic storm
  Density increase (3-8RE) in response to magnetic storm, reason unkown [Bailey and Gruntman, 2013]
  Timing of observation: 10days to 3 months after launch
  ② Quantising hydrogen atom supply process into exosphere
①and② leading to quantitative understanding of atmospheric loss proessより大気散逸過程の定量的理解

## Slide 9
MCP+RAE模式図 [Yoshioka et al., 2010]
LAICA：(Geocoronal Hydrogen)
Lyman Alpha Imaging CAmera
120mm
LAICA形状図
光学系：カセグレン望遠鏡
主鏡・副鏡ともに球面(Al+MgF2)
フードなしで迷光対策が必要
detector：same as that on Bepicolombo/MPO's PHEBUS/FUVと同型

## Slide 10
MCP+RAE模式図 [Yoshioka et al., 2010]
LAICA：(Geocoronal Hydrogen)
Lyman Alpha Imaging CAmera
120mm
LAICA形状図
optical system: casegrain telescope
both main and sub mirros are spherical (Al+MgF2)
no hood protection, so certain measures are required
detector: same as that on：Bepicolombo/MPO's PHEBUS/FUV
LAICA (PM)
80mm
118mm
focal lenngth: 400mm
field of view: 3 degrees
angular resolution: 0.024 dgrees
frequency range: 122+/-10nm
sensitivity: 3.4x10-3(cts/s/pix/R)
main mirror effective radius: 71mm
submirror effective radius: 32mm
mass: 2.14kg
power consumption: max 5W
300mmx160mmx130mm

## Slide 11
Spherical Cassegrain mirror
detector: approx. 160 µm per pixel
⇒spot diamter ＜160µm within FOV 3 degrees
spot diagram of optical system
light path outline
y
z
attachment precision
X,Ydirection: 1mm
Zdirection: 0.06mm

## Slide 12: strain light protection (lack of space)
↑beam entrance angle+/-1.5deg
↑no direct light path from entrance to detectorstrain light is less than 1/100 of hydrogen glow in interstellar space

## Slide 13
Optical system adhesion (Rikkyo U)
Primary/Secondary mirror & bandpass filter were attached using a space-qualified adhesive and glass beads (φ100 µm)
Primary mirror
Vibration, shock, and thermal tests
Temperature range：-20℃〜60℃
Vibration level：27 [Grms]
Shock level：1000 [G]
Adhesive and glass beads
・thickness control
・repeatability
Aluminum plate
Primary/Secondary mirror or Bandpass filter

## Slide 14
Adhesion of PM mirrors
Preparation of the adhesion
primary mirror(PM)
Preparation of the adhesion
secondary mirror(PM)
① Primary mirror
② Secondary mirror
Mixture of
Space-adhesive
& glass beads

## Slide 15
156µm
156µm
①
③
⑤
④
②
Focus adjustment
Spot size (FWHM)
① Center : 48.9µm
② Right : 66.3µm
③ Left : 69.6µm
④ Top : 97.4µm
⑤ Bottom: 68.3µm
(Requirement: 156µm )
Focus adjustment
Telescope
Lamp(visible light)
LAICA
(lens tube)
Collimated light
Camera(Sony α7)
→OK
high temp.(60 degrees)
is no problem

## Slide 16
Schedule od development
2013
Oct: Start, concept design
Nov: Design and testing of support structure
Dec: Vibration and impact testing of support structure
(adhesion strength, MCP impact level reduction)
2014
Jan: Final spec. confirmed, PM fabrication start
Feb: Temp. testing of adhesion points
Mar: PM cpmpleted and focus testing
completion of FM sensor(MCP+RAE) and support structure of read circuit
Apr: PM adhesion
May: FM tube structure completed and focus testing, QT vibration and impact testing, temp. testing (focus)
Jun: FM vibration test, thermal vacuum test, attaching to the probe
Dec: launch
[JAXA]
budget: yen 22 million

## Slide 17
Conclusion
・Geocorona distribution in wide range (~8Re20Re) unobtainable by earthbound satellites
・Global distribution with higher temporal resolution (12h2h) unobtainable by earthbound satellites
・Low cost and short period of development
(educational programme for students and myself)
・Hydrogen Ryaman alpha line by PROCYON imaging system
[annecdote] Sputonik with a dog on board was, at that time, said to be very careless and the dog died. Wether or not that project was a great success is uncertain, but it certainly did contribute towards later space programmes